Functional Block 3 — Mobile Robot (ASS_Robot)
Product design created by: Arno Gaelens
## Idea Behind the Product
When the wearable sensor detects a fall event, the robot must already be in the correct position to deploy the airbag effectively. A robot that arrives too late or from the wrong side cannot protect the user. The mobile robot solves this by continuously following the person and positioning itself at the rear-left side — the statistically most common fall direction — at all times.
The robot must operate in real indoor environments shared with furniture, walls and other people. It therefore needs to navigate autonomously, avoid obstacles and keep pace with a walking elderly person without being intrusive or creating a trip hazard itself.
The key idea is that the robot acts as a mobile airbag platform: it is not stationary like a bed rail or walker, but follows the person room to room, always ready. The upper section rotates independently so the airbag always faces the person regardless of the robot's driving direction.
## Working Principle
The robot is a differential-drive platform with a rotating upper body (Upper_Swivel). The lower chassis handles locomotion; the upper body carries the airbag module and a LiDAR sensor.
A wearable device worn by the user continuously broadcasts the user's position. The robot subscribes to this position and computes a target point 0.6 m behind and 0.35 m to the left of the person's heading. It drives toward this target using a reactive velocity controller — no pre-planned path, no map required. The upper swivel simultaneously rotates to always face the person, ensuring the airbag is correctly oriented at the moment of deployment.
The system integrates locomotion, sensing, person tracking and obstacle avoidance into one continuous control loop running at 10 Hz.
Although the robot is one integrated unit, it consists of multiple functional subsystems:
- Locomotion — differential drive wheels + passive castor
- Perception — 360° LiDAR
- Person tracking — reactive follower node
- Obstacle avoidance — potential field on raw LiDAR scan
- Upper body orientation — P controller on swivel joint
- Airbag mounting — Upper_Swivel carries the airbag module
### Forces During Operation
The chassis is exposed to drive motor reaction forces, wheel friction against the floor, and reaction forces when the airbag deploys. The castor absorbs minor floor irregularities.
### Temperature Management
Motors and electronics generate low heat during normal walking-pace operation. The airbag module's CO₂ discharge is isolated to the Upper_Swivel and handled by the airbag system's own thermal design.
### Kinematics
The lower chassis performs planar differential-drive motion (translation + rotation). The Upper_Swivel rotates continuously around the vertical axis relative to the chassis, driven by a velocity-controlled motor. No other joints are active.
## Person-Following Algorithm
### Target Point Computation
The robot does not follow the person directly. It targets a point offset from the person:
- 0.6 m behind the person along their heading direction
- 0.35 m to the left of the person
This ensures the robot is always pre-positioned on the most likely fall side.
### Linear Velocity Control
Distance error = distance to target − 0.1 m (desired standoff)
- Error > 0.05 m → drive forward proportionally, capped at 1.2 m/s
- Error < −0.05 m → reverse at up to −0.2 m/s
### Angular Velocity Control
Steering angle = angle to target in robot frame. Blended between person-tracking steering and obstacle repulsion based on proximity to nearest obstacle.
### Obstacle Avoidance (Potential Field)
Each LiDAR ray within ±100° and closer than 1.5 m generates a repulsive angular force:
- Weight = ((obs_dist − r) / obs_dist)²
- Forward-facing obstacles weighted more heavily
- Rays within 50° of person direction ignored if beyond 70% of person distance
- Speed reduction starts at 0.7 m from closest obstacle
- Hard reverse triggered below 0.4 m
### Upper_Swivel Tracking
Swivel error = angle to person − current swivel angle
Swivel velocity = 5.0 × error, capped at ±4 rad/s
This ensures the airbag faces the person at all times regardless of drive direction.
## Material Choices
Part	Material	Justification
Chassis frame	[to be filled — Al profile / steel sheet]	Rigidity, machinability
Wheel hubs	[to be filled]	—
Enclosure panels	[to be filled — ABS / sheet metal]	Impact resistance
Swivel bearing	[to be filled]	Continuous rotation under load
Fasteners	Stainless steel	Corrosion resistance, durability

Material section to be completed by mechanical design team from BOM in 0_ProjectInformation/
## Component Selection
### Drive Motors + Wheels
Field	Value
Component	Differential drive motors + wheels
Model & supplier	[to be filled from BOM]
Why this type	Differential drive provides simple, reliable planar navigation with zero turning radius
Characteristics	Wheel radius 69.5 mm • Wheel separation 498 mm • Max speed 1.5 m/s
Justification	Compact footprint, suitable for indoor use, well-supported in ROS2

### LiDAR Sensor
Field	Value
Component	2D LiDAR
Model & supplier	[to be filled from BOM]
Why this type	Provides 360° obstacle detection for safe navigation in cluttered indoor environments
Characteristics	360° scan • 10 Hz • 10 m range • Mounted on Upper_Swivel
Justification	Rotates with upper body so airbag side is always monitored; sufficient range and rate for walking-speed operation

### Onboard Computer
Field	Value
Component	Single-board computer / mini PC
Model & supplier	[to be filled]
Why this type	Runs ROS2 Jazzy, person-follower node and obstacle avoidance at 10 Hz in real time
Characteristics	Ubuntu 24.04 • ROS2 Jazzy • Sufficient CPU for sensor fusion and control loop
Justification	ROS2 ecosystem provides well-tested navigation, sensor drivers and communication infrastructure

### Swivel Motor + Controller
Field	Value
Component	Rotary actuator for Upper_Swivel
Model & supplier	[to be filled]
Why this type	Upper body must continuously rotate to keep airbag facing person
Characteristics	Velocity-controlled • ±4 rad/s operating range • ros2_control interface (JointGroupVelocityController)
Justification	Velocity control allows smooth P-controller tracking without position overshoots

### Battery
Field	Value
Component	Main drive battery
Model & supplier	[to be filled from BOM]
Why this type	Powers motors, computer and sensors for a full usage session
Characteristics	[voltage, capacity, chemistry — to be filled]
Justification	[to be filled]

## Data Management and Controls
Sensors: LiDAR (360°, 10 Hz, 10 m range), wheel encoders (via odometry), wearable wireless signal (person pose)
Controller: Onboard computer running ROS2 Jazzy
Control process:
1. Wearable broadcasts person position → received as /person_pose
2. Robot reads own position from wheel odometry → /odom
3. LiDAR publishes 360° scan → /scan
4. Person-follower node computes rear-left target from person heading
5. Potential field computes repulsive steering from nearby obstacles
6. Velocity command blended and published → /cmd_vel → drives wheels
7. Swivel P-controller computes rotation speed → upper body tracks person
8. Loop repeats at 10 Hz
## Accompanying Services
At prototype stage:
- Charging instructions for drive battery
- Basic wheel and joint maintenance
- Software update procedure (ROS2 workspace rebuild)
- Operating instructions for caregiver / operator
Future:
- Remote monitoring dashboard
- Automatic low-battery return to charging station
- Multi-robot coordination
## Implementation Plan
Phase	Description	Status
1	Gazebo simulation with LiDAR, odometry, cmd_vel, topic bridges	DONE
2	LiDAR visualization and scan validation	DONE
3	Mapless Nav2 integration (rolling costmaps, no AMCL)	DONE
4	Potential field obstacle avoidance + RViz costmap display	DONE
5	RViz configuration with auto-loaded config file	DONE
6	Person simulation — click-to-draw path, natural movement	DONE
7	Reactive person follower with rear-left offset positioning	DONE
8	Upper_Swivel continuous person tracking via P controller	DONE
9	Integration with wearable (replace sim pose with real BLE/Wi-Fi signal)	TODO
10	Integration with airbag trigger (connect follower output to deployment logic)	TODO
11	Real hardware deployment and tuning	TODO

## Cost
To be filled from 0_ProjectInformation/ BOM
Component	Model	Supplier	Qty	Price
Chassis	—	—	1	—
Drive motors	—	—	2	—
Wheels	—	—	2	—
Castor	—	—	1	—
LiDAR	—	—	1	—
Swivel motor	—	—	1	—
Onboard computer	—	—	1	—
Battery	—	—	1	—
Motor drivers	—	—	—	—
Fasteners / misc	—	—	—	—
TOTAL				—